## Slide 1: The Basics
Types of cameras

## Slide 2: Types of cameras
Film cameras
Digital cameras

## Slide 3: Types of cameras
Film cameras
  View camera
  Viewfinder camera
    Point and shoot or compact cameras
  Single lens reflex camera (SLR)
  Twin lens reflex camera (TLR)
  Specialty cameras

## Slide 4: Types of cameras
Digital cameras
  Viewfinder camera
    Point and shoot or compact cameras
  Single lens reflex camera (SLR)
    DSLR is the term for digital SLR cameras
    Specialty cameras

## Slide 5: View camera
Built like an accordion, with a lens in the front, a viewing screen in the back, and flexible bellows in between.

## Slide 6: View camera
ADVANTAGES
    Large film size (4x5, 5,7, 8x10)
    Sharp detail
    What you see in the viewfinder is exactly what you will get on the negative.
    You can change the position of the film and lens relative to each other to correct distortion.
DISADVANTAGES
    Bulky and heavy
    Must use a tripod.
    Image on the viewing screen is not bright so you have put a focusing cloth over your head and the back of the camera.
    The image appears reversed and upside down on the viewing screen.
    Rapid shooting is difficult.

## Slide 7: View camera
Used for:
    Commercial studio photography
    Landscapes
    Architectural photography

## Slide 8: Viewfinder
A compact, lightweight, camera that allows you to view the scene through a small window.
Viewfinder cameras include inexpensive point-and-shoot cameras

## Slide 9: Viewfinder
ADVANTAGES
    Compact, lightweight, and fast handling.
    Quieter than an SLR
    Bright viewfinder image allows easy focusing.
DISADVANTAGES
    Parallax error - Because the viewfinder is in a different position than the lens, you cannot see exactly what the lens sees. The closer the subject the more evident the parallax.

## Slide 10: Single lens reflex
An SLR has a mirror and pentaprism that allow you to use the lens for viewing and focusing.
Most are 35mm, but some are medium format.

## Slide 11: Single lens reflex
ADVANTAGES
    Eliminates parallax - what you see is what you will get.
    Easy to focus.
    Usually has a built-in light meter.
DISADVANTAGES
    Heavier and larger than a rangefinder.
    Relatively complex with many parts that may need repair.
    The mirror movement makes the camera loud and causes vibration.
    Momentary black-out at the time of exposure.

## Slide 12: Twin lens reflex
A TLR has a fixed mirror that reflects the scene upward onto a viewing screen.
There is one lens to expose the film and another to view the image.

## Slide 13: Twin lens reflex
ADVANTAGES
    Fixed mirror allows quiet operation.
    Simple, rugged construction.
    The viewing screen placement on top allows you to easily photograph from the ground or other awkward angles.
    Medium-format film.
DISAVANTAGES
    Parallax
    It is difficult to follow moving objects because the image on the screen is reversed left to right.
    It is a larger camera that can be somewhat cumbersome.
    Difficult to use at eye level.

## Slide 14: Specialty camera
Used for a specific purpose
Underwater cameras
Panoramic cameras
Polaroid Cameras

## Slide 15: Specialty camera
Used for a specific purpose
Underwater cameras

## Slide 16: Specialty camera
Used for a specific purpose
Panoramic cameras

## Slide 17: Specialty camera
Used for a specific purpose
Polaroid Cameras

## Slide 18: Summary
You should be able to name the four types of cameras.
Can you name some examples of specialty cameras and their uses?

## Slide 19: Types of cameras

## Slide 20: Types of cameras

## Slide 21: Types of cameras

## Slide 22: Types of cameras

## Slide 23: Types of cameras

## Slide 24: Types of cameras

## Slide 25: Types of cameras

## Slide 26: Types of cameras

## Slide 27: Types of cameras